## Slide 1: TACK: Improving Wireless Transport Performance by Taming Acknowledgments
Tong Li♥, Kai Zheng♥, Ke Xu, Rahul Arvind Jadhav♥,
Tao Xiong♥, Keith Winstein, Kun Tan♥
acm sigcomm
August 10–14, 2020
♦
♠
Notes: Hi, my name is Tong Li. Today I am going to introduce TACK: Improving Wireless Transport Performance by Taming Acknowledgments.

## Slide 2: High Speed Rails (HSRs)
Wireless local area network (WLAN) demands high throughput
100
Mbps
Average
200
Mbps
Peek
500
Mbps
UHD VR
30
Mbps
2018
92
Mbps
2023
Application Requirements | UHD Cameras (Security) | UHD Streaming | VR Streaming | Self Driving Vehicle Diagnostics | Cloud Gaming | UHD IP Video | 8K Wall TV | HD VR | UHD VR
Average (Mbps) | 16 | 16 | 17 | 20 | 30 | 51 | 100 | 167 | 500
Source: Cisco Annual Internet Report, 2018–2023
8K Videos from Youtube | Asteroid Discovery | NORWAY | The Las Vegas Strip | TOKYO HDR Time Lapse | Angel Falls, Venezuela | Tigers Go For A Swim | Henosis(8K Short Film)
Average (Mbps) | 81.0 | 81.1 | 129.1 | 62.8 | 57.7 | 72.0 | 40.6
Peek (Mbps) | 206.9 | 196.9 | 134.2 | 83.2 | 81.3 | 72.1 | 71.1
Source: Huawei iLab, 2017
Ultra-high-definition
(UHD) wireless projection
VR interactive gaming
AR interactive gaming
Notes: High-throughput transport over WLAN becomes a demanding requirement with the emergence of applications such as UHD wireless projection, and VR/AR-based interactive gaming.
Particularly, the average throughput requirement is 100 megabits per second of an 8K video, whose peak throughput requirement might reach 200 megabits per second.
For a UHD VR-based application, the throughput even reach 500 megabits per second.
It is reported that the average WLAN connection speed in 20,18 was 30 megabits per second and will be more than triple by 20,23. Which, however, is still far from satisfactory for UHD-video-based applications.

## Slide 3: TCP ACKs cause internal interference
External Interference：Between wireless devices on the same channel
Internal Interference： Between data packets and ACKs in the same connection
External Interference
TCP forward path：Data packets
TCP backward path：
ACK packets
Internal Interference
ACK: ACKnowledgement
Notes: Most modern WLANs are based on the IEEE 802.11 standards. It is well-studied that medium access overhead in WLAN can significantly reduce TCP throughput, this is because TCP ACKs cause internal interference on the transport layer.

## Slide 4: ACKs cause similar medium access overhead
Time
Contention window
(random back off)
Inter-frame space
(IFS)
Extra overhead for sending each packet
Last frame
Next frame
Medium acquisition overhead in WLAN based on the IEEE 802.11 medium access control (MAC) protocol
independent with packet size
Notes: When frames are operated in the MAC layer, the time period including the inter-frame space and a random back-off period is the extra overhead between completion of the last frame and starting of the next frame.
【】Since the extra overhead for sending each packet is independent with packet size, ACKs cause almost similar medium access overhead despite the much smaller size. As a result, the internal interference between data packets and ACKs is non-negligible.

## Slide 5: Reducing ACK frequency improves throughput
(b) Data throughput
(a) ACK throughput
ACK frequency increases
Experiments for contention between data packets and ACKs over 802.11n wireless links
  *Data is collected by a UDP-based simulation tool Ackemu (https://github.com/fillthepipe/ackemu)
Notes: Basically, TCP sends an ACK for every one or two packets which is frequent. As shown in the left figure,
【】the throughput on the ACK path is relatively low, however, as shown in the right figure,
【】the throughput on the data path decreases significantly with the increase of ACK frequency.

## Slide 6: But, simply reducing ACK frequency hurts TCP performance
throughput (Mbps)
Idea goodput with reduced ACK frequency
Actual goodput with reduced ACK frequency but without advancements
Goodput
of legacy TCP
Positive Effect
Negative Effect
TCP’s transport control depends on frequent ACKs
“A TCP receiver which does not generate an ACK for every second full-sized segment exhibits a "Stretch ACK Violation".
--- 1999, RFC 2525, Vern Paxson et.al
Reducing ACK frequency has both “positive effect” and “negative effect”
Notes: In wireless scenarios, reducing ACK frequency has a “positive effect” on the transport performance due to the reduced contentions.
Unfortunately, simply reducing ACK frequency hurts TCP performance, which is called negative effect. This negative effect is because that TCP’s transport control depends on frequent ACKs and the transport is disturbed when ACK frequency is excessively reduced.

## Slide 7: So, let’s tame acknowledgements
Goal:
Seek the optimized ACK frequency that is exactly required and a corresponding acknowledgement mechanism that avoids the “negative effect”
Notes: In this case, acknowledgements should be tamed. This paper aims to seek the optimized ACK frequency that is exactly required
and a corresponding acknowledgement mechanism that avoids the “negative effect”.

## Slide 8: Two ways to reduce ACK frequency (f)
Byte-counting ACK
f: ACK frequency with unit of Hz, i.e., number of ACKs per second
L: number of full-sized packets counted before sending an ACK
Periodic ACK
MSS: maximum segment size
bw: data throughput
𝛼: time interval between two ACKs
ACK
ACK
ACK
ACK
Data
(L=1)
(L=2)
(L=3)
Notes: ACK frequency can be denoted by f with the unit of Hz, that is, the number of ACKs per second, which can be reduced in two fundamental ways: byte-counting ACK and periodic ACK.
【】Byte-counting ACK reduces ACK frequency by sending an ACK for every two or more incoming full-sized packets. The frequency is proportional to data throughput.
【】We can also reduce ACK frequency by sending an ACK for each time interval, that is, periodic ACK.

## Slide 9: Not bounded or not minimized under bandwidth change
Byte-counting ACK
periodic ACK
0
∞
∞
Constant
f: ACK frequency with unit of Hz, i.e., number of ACKs per second
L: number of full-sized packets counted before sending an ACK
MSS: maximum segment size
bw: data throughput
𝛼: time interval between two ACKs
Notes: However, for byte-counting ACK, when data throughput is high,
【】the ACK frequency still might be large. On the other hand, for periodic ACK,
【】when data throughput is low,
【】ACK frequency is always as high as that in the case of a high throughput, which wastes resources.
In summary, the frequency of both ways is not bounded or not minimized under bandwidth change.

## Slide 10: ACK frequency minimization
Combining the above two ways to minimize ACK frequency
0
∞
Constant
0
f: ACK frequency with unit of Hz, i.e., number of ACKs per second
L: number of full-sized packets counted before sending an ACK
MSS: maximum segment size
bw: data throughput
𝛼: time interval between two ACKs
Notes: To control ACK frequency in the context of network dynamics, we combine the above two ways to minimize ACK frequency.
【】When data throughput is high,
【】the ACK frequency is bounded. On the other hand,
【】when data throughput is low,
【】the ACK frequency is reduced proportionally.

## Slide 11: Tame ACK (TACK)
(Byte-counting ACK)
(periodic ACK)
: the maximum bandwidth estimate
: the minimum RTT estimate
: the number of ACKs per
: the bandwidth and delay product
Notes: We propose TACK, an instance whose frequency is decided by bdp, the bandwidth and delay product.
【】Qualitatively, TACK applies periodic ACK when bdp is large,
【】and falls back to byte-counting ACK when bdp is small.

## Slide 12: How is TACK’s “positive effect”?
Various wireless links: IEEE 802.11 b/g/n/ac
Method
  To better estimate TACK’s “positive effect”, we build a UDP-based simulation tool Ackemu to assure that there is no “negative effect”
  Ackemu (https://github.com/fillthepipe/ackemu)
    Ackemu sender keeps sending 1518-byte UDP packets
    When trigger condition is met, Ackemu receiver sends one 64-byte UDP packet as an ACK
Notes: To better estimate TACK’s “positive effect” over various wireless links, we build a UDP-based tool to assure that there is no “negative effect”. The sender keeps sending large UDP packets, and the receiver has implemented various ACK thinning technologies including TACK. When the trigger condition is met, the receiver sends one small UDP packet as an ACK.

## Slide 13: TACK reduces ACK frequency significantly
Quantitative analysis of TACK frequency over IEEE 802.11 b/g/n/ac wireless links
PHY rate increases
Notes: The result is that
more number of ACKs are reduced in the case of a faster physical rate.
【】For example, TACK has the same frequency as TCP’s delayed ACK over 802.11b links with a small RTT.
【】However, for the 802.11ac links, the frequency of TACK has dropped two orders of magnitude when RTT is 10ms
【】and three orders of magnitude when RTT is 80 ms.

## Slide 14: Ideally, TACK improves goodput
(RTT=80 ms, IEEE 802.11n)
transport upper bound
Ideal goodput without “negative effect”: Transport control will not be disturbed by reducing ACK frequency
Notes: Ideally, links with faster physical rate enlarge goodput improvement. TACK approaches the transport upper bound with a minimized ACK frequency.

## Slide 15: How to avoid TACK’s “negative effect”?
Issues in loss recovery
Issues in round-trip timing
Issues in send rate control
Reducing ACK frequency enlarges feedback delay upon loss events. ACK loss or retransmission loss doubles the delay
Generating only one RTT sample among multiple packets is likely to result in biases
CC: The fewer ACKs sent, the larger the bursts of packets released
FC: Delay acknowledging packet receipts and reporting rwnd, resulting in feedback lags and bandwidth under-utilization
Notes: To apply TACK without “negative effect”, we list several major issues to handle in terms of loss recovery, round-trip timing,
and send rate control including congestion control and flow control. Next, we will give some case studies to better understand these issues.

## Slide 16: Enlarged delay in loss recovery
Sender
Receiver
Receiver’s APP
Packet 3 blocks the head of line (8 subsequent packets)
Packet 1~11
ACK2
Packet 1
Packet 2
Packet 3
Packet 3~11
Retransmit Packet 3
ACK3
ACK3
ACK3
ACK3
Packet 12
Packet 12
delay of packet reassembling
Case study: Legacy TCP
Notes: It is well-known that head-of-line blocking incurs high delay of packet reassembling and thus leads to transport performance decline. In the case of legacy TCP, the loss of packet 3 blocks the head of line with 8 subsequent packets.

## Slide 17: Enlarged delay in loss recovery
Sender
Receiver
Receiver’s APP
Packet 3 blocks the head of line (97 subsequent packets)
Packet 1~100
TACK1
Packet 1
Packet 2
TACK2
delay of packet reassembling
Packet 3
Packet 3~100
Packet 3
…
…
Packet 101
Retransmit Packet 3
Case study: TACK
Notes: Since TACK might be excessively delayed. Applying TACK will further enlarge this delay incurred by head-of-line blocking. In the case of TACK, the loss of packet 3 blocks the head of line with 97 subsequent packets. When loss occurs during the TACK interval, the excessive TACK delay disturbs loss detection, resulting in costly retransmission timeouts. TACK loss further aggravates this problem.

## Slide 18: Biased round-trip timing
TACK-based round-trip timing: A case study
Notes: In terms of round-trip timing, the initial RTT can be computed during handshakes,
【】after that, the sender calculates an RTT sample upon receiving a TACK.
【】The problem here is that multiple data packets might be received during the TACK interval, generating only one RTT sample among multiple packets is likely to result in biases. For example, a larger minimum RTT estimate or a smaller maximum RTT estimate. In general, the higher the throughput, the larger the biases.

## Slide 19: Burst send pattern
time
ACK
Data packet
ACK Interval
time
ACK1
ACK2
ACK4
ACK5
ACK6
ACK7
ACK3
ACK Interval
TACK1
TACK2
Frequent ACK
Infrequent ACK
Data packet
ACK
Burst send pattern
Notes: Third, for congestion control, a burst of packets can be sent in response to a single delayed ACK. Since TACK might be excessively delayed, the burst send pattern may cause larger buffer requirement, higher loss rate, and longer queueing delay if not carefully handled.

## Slide 20: Delayed send window update
buffered data
free buffer space
AWND
RcvBuffer
Data packets
Application
Receive buffer
Sender
Receiver
TACK1
RcvBuffer released
Stop sending
rwnd=0
Delayed update
rwnd=100
Delayed send window update
TACK2
Notes: For send window update, TCP ACKs report the announcement window in the TCP header for flow control. Reducing ACK frequency might also lead to feedback lags and bandwidth under-utilization. For example, TACK is sent every 50 ms. Assume a TACK notifies a zero window due to the receive buffer runs out, upon receiving this TACK, the sender stops sending data. In the case that the receiver buffer is released 5 ms after sending TACK1 due to loss recovery, the sender continues to be blocked for another 45 ms until TACK2 is sent, and thus wastes opportunity of sending data. TACK loss further aggravates this issue.

## Slide 21: TACK-based acknowledgement mechanism
Applying TACK significantly reduces ACK frequency and improves performance ideally
Independently applying TACK probably falls short
WLAN requires a full TACK-based acknowledgement mechanism that overcomes the hurdles for applying TACK, using a controlled frequency of ACKs to support efficient transport
Notes: To summarize, applying TACK significantly reduces ACK frequency and improves performance ideally.
【】However, as discussed above, independently applying TACK probably falls short of robust loss recovery, accurate round-trip timing, and effective send rate control.
【】What we really want, for WLAN, is a full TACK-based acknowledgement mechanism that overcomes the hurdles for applying TACK, using a controlled frequency of ACKs to support efficient transport. There are some notable features of the TACK-based acknowledgement mechanism which are important for reasoning about the differences from legacy TCP. We briefly describe these features below.

## Slide 22: Features of TACK-based acknowledgement mechanism
More types of ACKs
  Apart from the ACK type of TACK, also introduce the ACK type of IACK (“Instant ACK”）
  IACK and TACK are complementary
More necessary information carried in ACKs
  Carry more contiguous range of lost packets when ACK loss rate has reached a critical level
  Sync ACK delay, timestamp, loss rate, delivery rate, etc. between endpoints
Less number of ACKs, but are exactly what are required by transport
  IACK is instant event-driven , whose frequency is usually low and negligible
The design rationale: an analogy
Notes: First, apart from the ACK type of TACK, we also introduce the ACK type of IACK to assure timely feedback upon instant events. IACK and TACK are complementary. IACK assures timely signaling while TACK acts as the last resort mechanism in the case of ACK loss.
Second, when the loss rate on the ACK path has reached a critical level, TACK should carry more information such as contiguous range of lost packets orreceived packets.
With more types of ACKs and more necessary information carried in ACKs, the TACK-based acknowledgement mechanism therefore is able to send less number of ACKs but are exactly what are required by transport.

## Slide 23: Advancements to decrease dependence on frequent ACKs
5
6
7
8
Send
Loss Recovery
Round-trip Timing
Send Rate Control
Feedback Handling
Send
Buffer
1
2
3
4
Receive
Buffer
TACK-based ACK Mechanism
Receive
Monitor
TACK/IACK
Data Packet
Data
Data
Sender
Receiver
Advancements in loss recovery
  Packet number, TACK+IACK
Advancements in round-trip timing
  One-way delay as auxiliary
Advancements in send rate control
  Congestion control: Pacing
  Flow control: IACK
Framework: TACK-based protocol design
Notes: For TACK-based protocol design, the advancements in loss recovery, round-trip timing, and send rate control are the most key reasons that TCP’s dependence on frequent ACKs has decreased.

## Slide 24: Advancements in round-trip timing
  Overhead
  Accuracy
  0
RTT sampling of the largest acked packet
Per-packet RTT sampling
20 | 16 | 22 | 15 | 30
15
10 | 11 | 20 | 7.5 | 8
OWD samples
RTT samples
Sender
Receiver
Data
packet
ACK
Sender
Receiver
RTTmin sample
  Better
This paper
Legacy way: sender-side RTT sampling
This paper: receiver-side one-way delay (OWD) sampling without maintaining too many states
Carry timestamps for a packet who achieves OWDmin
Design Rationale: Variation of OWD reflects the variation of RTT
Notes: Take the minimum RTT estimation as an example. The legacy way of sender-side RTT sampling is either inaccurate or expensive.
In this paper, we sample the one-way delay at the receiver, and the TACK carries the timestamps for a packet who achieves the minimum one-way delay. The sender then generates the minimum RTT sample according to this TACK.
【】Because TACK only carries the necessary information, the TACK-based protocol design not only reduces overhead, but also ensures accuracy.

## Slide 25: Other advancements in TACK-based protocol design
Advancements in loss recovery
  Packet number enables receiver-based loss detection
  IACK speeds up loss recovery on lossy data path
  TACK assures loss recovery robustness on bidirectionally lossy path
  Advancements in send rate control
  Pacing
  An IACK updating the AWND should be sent without delay when encountering an abrupt change of receive buffer
  For more details, please refer to the paper
Notes: For other advancements in TACK-based protocol, we adopt a receiver-based loss detection, in which the packet number, the IACK, and the TACK play different roles. Packet number enables receiver-based loss detection, IACK speeds up loss recovery, and TACK assures loss recovery robustness.
In order to control the amount of sent data, TACK-based congestion controller should integrate with pacing instead of the burst send pattern. Also, an IACK updating the announcement window should be sent without delay when the receive buffer runs out. For more details, please refer to the paper.

## Slide 26: Evaluation
TCP-TACK implementation
  TCP-TACK: A TCP implementation that applies TACK and deploys the advancements as specified above
  Co-design the receiver-based BBR as a TACK-based congestion controller
  𝐿 = 2, 𝜷=4
Experiment setup
  TCP BBR represents TCP using BBR as congestion controller and RACK as loss detection algorithm
  New BPF socket option, BPF_SOCK_OPS_ACK_THRESH_INIT, to allow changing the TCP ACK frequency (https://github.com/fillthepipe/TcpAckThinning)
  Wireless tests are in a public room with over 10 additional APs and over 100 wireless users at peak time. Ping test shows that the RTT varies between 4 to 200 ms and slight burst losses exist
Notes: For evaluation, we implement TCP-TACK, a TCP implementation that applies TACK and deploys the advancements as specified above. We co-design the receiver-based BBR as a TACK-based congestion controller. We introduce a new BPF socket option to allow changing the TCP ACK frequency. Wireless tests are in a public room with some interferences.

## Slide 27: TACK-based protocol in WLAN
Percentage of goodput improvement of
TCP-TACK over TCP-BBR in WLAN
Notes: Here is the result. TCP-TACK achieves significant advantages over legacy TCP in WLAN scenarios due to less contention between data packets and ACKs. Specifically, TCP-TACK reduces over 90% of ACKs and also obtains an improvement of 28% on goodput.

## Slide 28: TACK-based protocol in WAN
Violin-plots of performance ranking
(Results are from data traces during 200 days: https://pantheon.stanford.edu/summary)
Notes: We further find it performs equally well as high-speed TCP variants in wide area network scenarios, this is attributed to the advancements of the TACK-based protocol design in loss recovery, round-trip timing, and send rate control. This serves as a strong validation of TACK.

## Slide 29: Key Takeaways
WLAN transport can be improved on the transport layer by reducing the ACK frequency required
Ideally, TACK improves goodput due to significantly reducing ACK frequency
Actually, independently applying TACK hurts TCP performance
Advanced TACK-based protocol provides a good replacement of legacy TCP to compensate for scenarios where the acknowledgement overhead is non-negligible
Notes: To conclude, this paper aims to improve the WLAN transport on the transport layer by reducing the ACK frequency required.
【】We find that, ideally, TACK improves goodput due to significantly reducing ACK frequency.
【】However, independently applying TACK hurts TCP performance.
【】Thus we design the advanced TACK-based protocol and demonstrate that it is a good replacement of legacy TCP to compensate for scenarios where the acknowledgement overhead is non-negligible.

## Slide 30: Thank You! Email: li.tong@huawei.com Q & A
Notes: That’s all for my report, thank you for your attention.