## Slide 1: TACK: Improving Wireless Transport Performance by Taming Acknowledgments
Tong Li♥, Kai Zheng♥, Ke Xu, Rahul Arvind Jadhav♥,
Tao Xiong♥, Keith Winstein, Kun Tan♥
acm sigcomm
August 10–14, 2020
♦
♠
Notes: Hi, I am Tong Li from Huawei. Today I am going to introduce TACK:
Improving Wireless Transport Performance by Taming Acknowledgments.

## Slide 2: High Speed Rails (HSRs)
Wireless local area network (WLAN) demands high throughput
100
Mbps
Average
200
Mbps
Peek
500
Mbps
UHD VR
30
Mbps
2018
92
Mbps
2023
Application Requirements | UHD Cameras (Security) | UHD Streaming | VR Streaming | Self Driving Vehicle Diagnostics | Cloud Gaming | UHD IP Video | 8K Wall TV | HD VR | UHD VR
Average (Mbps) | 16 | 16 | 17 | 20 | 30 | 51 | 100 | 167 | 500
Source: Cisco Annual Internet Report, 2018–2023
8K Videos from Youtube | Asteroid Discovery | NORWAY | The Las Vegas Strip | TOKYO HDR Time Lapse | Angel Falls, Venezuela | Tigers Go For A Swim | Henosis(8K Short Film)
Average (Mbps) | 81.0 | 81.1 | 129.1 | 62.8 | 57.7 | 72.0 | 40.6
Peek (Mbps) | 206.9 | 196.9 | 134.2 | 83.2 | 81.3 | 72.1 | 71.1
Source: Huawei iLab, 2017
Ultra-high-definition
(UHD) wireless projection
VR interactive gaming
AR interactive gaming
Notes: High-throughput transport over WLAN becomes a demanding requirement
with the emergence of applications such as UHD wireless projection,
VR/AR-based interactive gaming, and so on.
Particularly, the average throughput requirement is 100 megabits per second of an 8K video,
whose peak throughput requirement might reach 200 megabits per second.
For a UHD VR-based application, the throughput even reach 500 megabits per second.
It is reported that the average WLAN connection speed in 20,18 was 30 megabits per second
and will be more than triple by 20,23.
Which, however, is still far from satisfactory for UHD-video-based applications.

## Slide 3: TCP ACKs cause internal interference
External Interference：Between wireless devices on the same channel
Internal Interference： Between data packets and ACKs in the same connection
External Interference
TCP forward path：Data packets
TCP backward path：
ACK packets
Internal Interference
ACK: ACKnowdedgement
Notes: Most modern WLANs are based on the IEEE 802.11 standards.
It is well-studied that medium access overhead in WLAN can significantly reduce TCP throughput,
this is because TCP ACKs cause internal interference on the transport layer.

## Slide 4: ACKs cause similar medium access overhead
Time
Contention window
(random back off)
Inter-frame space
(IFS)
Extra overhead for sending each packet
Last frame
Next frame
Medium acquisition overhead in WLAN based on the IEEE 802.11 medium access control (MAC) protocol
independent with packet size
Notes: When frames are operated in the MAC layer,
the time period including the inter-frame space and a random back-off period is the extra overhead
between completion of the last frame and starting of the next frame.
【】Since the extra overhead for sending each packet is independent with packet size,
ACKs cause almost similar medium access overhead despite the much smaller size.
As a result, the internal interference between data packets and ACKs is non-negligible.

## Slide 5: Reducing ACK frequency improves throughput
(b) Data throughput
(a) ACK throughput
ACK frequency increases
Experiments for contention between data packets and ACKs over 802.11n wireless links
  *Data is collected by a UDP-based simulation tool Ackemu (https://github.com/fillthepipe/ackemu)
Notes: Basically, TCP sends an ACK for every one or two packets which is frequent.
As shown in the left figure,
【】the throughput on the ACK path is relatively low, however, as shown in the right figure,
【】the throughput on the data path decreases significantly with the increase of ACK frequency.

## Slide 6: But, simply reducing ACK frequency hurts TCP performance
throughput (Mbps)
Idea goodput with reduced ACK frequency
Actual goodput with reduced ACK frequency but without advancements
Goodput
of legacy TCP
Positive Effect
Negative Effect
TCP’s transport control depends on frequent ACKs
“A TCP receiver which does not generate an ACK for every second full-sized segment exhibits a "Stretch ACK Violation".
--- 1999, RFC 2525, Vern Paxson et.al
Reducing ACK frequency has both “positive effect” and “negative effect”
Notes: In wireless scenarios,
reducing ACK frequency has a “positive effect” on the transport performance
due to the reduced contentions.
Unfortunately, simply reducing ACK frequency hurts TCP performance,
which is called negative effect.
This negative effect is because that TCP’s transport control depends on frequent ACKs
and the transport is disturbed when ACK frequency is excessively reduced.

## Slide 7: So, let’s tame the acknowledgements
Goal:
Seek the optimized ACK frequency that is exactly required and a corresponding acknowledgement mechanism that avoids the “negative effect”
Notes: In this case, let’s tame the acknowledgements.
This paper aims to seek the optimized ACK frequency that is exactly required
and a corresponding acknowledgement mechanism that avoids the “negative effect”.

## Slide 8: Tame ACK (TACK)
(Byte-counting ACK)
(periodic ACK)
: the maximum bandwidth estimate
: the minimum RTT estimate
: the number of ACKs per
bdp: the bandwidth and delay product ()
f: ACK frequency with unit of Hz, i.e., number of ACKs per second
L: number of full-sized packets counted before sending an ACK
Notes: We propose TACK, a new acknowledgement whose frequency is decided by bdp (the bandwidth and delay product).
【】Qualitatively, TACK applies periodic ACK when bdp is large,
【】and falls back to byte-counting ACK when bdp is small.

## Slide 9: How is TACK’s “positive effect”?
Various wireless links: IEEE 802.11 b/g/n/ac
Method
  To better estimate TACK’s “positive effect”, we build a UDP-based simulation tool Ackemu to assure that there is no “negative effect”
  Ackemu (https://github.com/fillthepipe/ackemu)
    Ackemu sender keeps sending 1518-byte UDP packets
    When trigger condition is met, Ackemu receiver sends one 64-byte UDP packet as an ACK
Notes: First, to better estimate TACK’s “positive effect” over various wireless links,
we build a UDP-based tool to assure that there is no “negative effect”.
The sender keeps sending large UDP packets,
and the receiver has implemented various ACK thinning technologies including TACK.
When the trigger condition is met,
the receiver sends one small UDP packet as an ACK.

## Slide 10: TACK reduces ACK frequency significantly
Quantitative analysis of TACK frequency over IEEE 802.11 b/g/n/ac wireless links
PHY rate increases
Notes: The result is that more number of ACKs are reduced in the case of a faster physical rate.
【】For example, TACK has the same frequency as TCP’s delayed ACK over 802.11b wireless links with a small RTT.
【】However, for the 802.11ac links, the frequency of TACK has dropped two orders of magnitude when RTT is 10 ms
【】and three orders of magnitude when RTT is 80 ms.

## Slide 11: Ideally, TACK approaches transport bound
(RTT=80 ms, IEEE 802.11n)
transport upper bound
Ideal goodput without “negative effect”: Transport control will not be disturbed by reducing ACK frequency
Notes: Ideally, links with faster physical rate enlarge goodput improvement. TACK approaches the transport upper bound with a minimized ACK frequency.

## Slide 12: How to avoid TACK’s “negative effect”?
Issues in loss recovery
Issues in round-trip timing
Issues in send rate control
Reducing ACK frequency enlarges feedback delay upon loss events. ACK loss or retransmission loss doubles the delay
Generating only one RTT sample among multiple packets is likely to result in biases
CC: The fewer ACKs sent, the larger the bursts of packets released
FC: Delay acknowledging packet receipts and reporting rwnd, resulting in feedback lags and bandwidth under-utilization
Notes: As discussed above,
applying TACK not only has significant “positive effect”,
but also might have “negative effect”.
To avoid TACK’s “negative effect”,
we list several major issues to handle in terms of loss recovery, round-trip timing,
and send rate control including congestion control and flow control.
For detailed case studies of these issues, please refer to the paper.

## Slide 13: Not TACK, but TACK-based acknowledgement mechanism
More types of ACKs
  Apart from the ACK type of TACK, also introduce the ACK type of IACK (“Instant ACK”）
  IACK and TACK are complementary
More necessary information carried in ACKs
  Carry more contiguous range of lost packets when ACK loss rate has reached a critical level
  Sync ACK delay, timestamp, loss rate, delivery rate, etc. between endpoints
Less number of ACKs, but are exactly what are required by transport
  IACK is instant event-driven , whose frequency is usually low and negligible
The design rationale: an analogy
Notes: Since independently applying TACK probably falls short,
we propose a full TACK-based acknowledgement mechanism.
There are some notable features of this mechanism
which are important for reasoning about the differences from legacy TCP.
First, apart from the ACK type of TACK,
we also introduce the ACK type of IACK
to assure timely feedback upon instant events.
IACK and TACK are complementary.
IACK assures timely signaling
while TACK acts as the last resort mechanism in the case of ACK loss.
Second, when the loss rate on the ACK path has reached a critical level,
TACK should carry more information
such as contiguous range of lost packets or received packets.
With more types of ACKs and more necessary information carried in ACKs,
the TACK-based acknowledgement mechanism
therefore is able to send less number of ACKs
but are exactly what are required by transport.

## Slide 14: TACK-based protocol design
5
6
7
8
Send
Loss Recovery
Round-trip Timing
Send Rate Control
Feedback
Handling
Send
Buffer
1
2
3
4
Receive
Buffer
TACK-based ACK Mechanism
Receive
Monitor
TACK/IACK
Data Packet
Data
Data
Sender
Receiver
Advancements in loss recovery
  Packet number, TACK+IACK
Advancements in round-trip timing
  One-way delay as auxiliary
Advancements in send rate control
  Congestion control: Pacing
  Flow control: IACK
Goal: Decrease TCP’s dependence on frequent ACKs
Notes: We also propose the TACK-based protocol design,
in which the advancements in loss recovery, round-trip timing, and send rate control
are the most key reasons
that TCP’s dependence on frequent ACKs has decreased.
For more technical details, please refer to the paper.

## Slide 15: Evaluation
TCP-TACK implementation
  TCP-TACK: A TCP implementation that applies TACK and deploys the advancements as specified above
  Co-design the receiver-based BBR as a TACK-based congestion controller
  𝐿 = 2, 𝜷=4
Experiment setup
  TCP BBR represents TCP using BBR as congestion controller and RACK as loss detection algorithm
  New BPF socket option, BPF_SOCK_OPS_ACK_THRESH_INIT, to allow changing the TCP ACK frequency (https://github.com/fillthepipe/TcpAckThinning)
  Wireless tests are in a public room with over 10 additional APs and over 100 wireless users at peak time. Ping test shows that the RTT varies between 4 to 200 ms and slight burst losses exist
Notes: For evaluation,
we implement TCP-TACK, a TCP implementation
that applies TACK and deploys the advancements as specified above.
We co-design the receiver-based BBR as a TACK-based congestion controller.
We also introduce a new BPF socket option to allow changing the TCP ACK frequency.
Wireless tests are in a public room with some interferences.

## Slide 16: TACK-based protocol in WLAN
Percentage of goodput improvement of
TCP-TACK over TCP-BBR in WLAN
Notes: Here is the result.
TCP-TACK achieves significant advantages over legacy TCP in WLAN scenarios
due to less contention between data packets and ACKs.
Specifically, TCP-TACK reduces over 90% of ACKs
and also obtains an improvement of 28% on goodput.

## Slide 17: TACK-based protocol in WAN
Violin-plots of performance ranking
(Results are from data traces during 200 days: https://pantheon.stanford.edu/summary)
Notes: We further find it performs equally well as
high-speed TCP variants in wide area network scenarios,
this is attributed to the advancements of the TACK-based protocol design
in loss recovery, round-trip timing, and send rate control.
This serves as a strong validation of TACK.

## Slide 18: Key Takeaways
WLAN transport can be improved on the transport layer by reducing the ACK frequency required
Ideally, TACK improves goodput due to significantly reducing ACK frequency
Actually, independently applying TACK hurts TCP performance
Advanced TACK-based protocol provides a good replacement of legacy TCP to compensate for scenarios where the acknowledgement overhead is non-negligible
Notes: To conclude,
this paper aims to improve the WLAN transport on the transport layer
by reducing the ACK frequency required.
【】We find that, ideally,
TACK improves goodput due to significantly reducing ACK frequency.
【】However, independently applying TACK hurts TCP performance.
【】Thus we design the advanced TACK-based protocol
and demonstrate that it is a good replacement of legacy TCP
to compensate for scenarios
where the acknowledgement overhead is non-negligible.

## Slide 19: Thank You! Email: li.tong@huawei.com Q & A
Notes: That’s all for my report, thank you for your watching!